# Text boxes

System for geological or biological exploration of the deep ocean floor, applicable also in rough floor morphology. Photos and real time TV pictures are usually taken in 
3-5 m distance from the seafloor. In addition, continuous measurements of scientific parameters can be taken and transmitted to the shipboard units.

| Equipment Pool No.: 001 |
| --- |
| Operational daily rates in DM | Rate in DM |
| less 11 days | 11-45 days | over 45 days | Transit | Mob/Demob (Lump Sum) |
| 1500,00* | 1000,00* | 800,00* | 500,00* | 4125,00* |
| * This offer is based on our prevailing general contract conditions |

Technical Data:

Operation depth	6000 m

Size	1.6 m (L) x 1.2 m (W) x 1.4 m (H)

Weight                  	520 kg, in air

350 kg, in water

Operation of OFOS

heaving and lowering speed, approx. 0.8 m/s (which corresponds to 
20-25 minutes per 1000 m water depth)

recommended operation time at seafloor: up to 4-6 hours (accumulator capacity is typically sufficient for this amount of time, depending upon power consumption of flood lights)

recharging of an accumulator set requires approx. 12 hours, therefore at least 
2 sets of accumulators are recommended

The system is presently equipped with:

Low light level TV camera

Flood lights

Photo camera, capacity 800 pictures

Deep-sea flash lights

Ground distance sonar

CTD probe (measurement of conductivity, temperature and depth )

2 deep-sea batteries (12 V, 230 Ah each)